## Slide 1: INTRODUCTION Chemical Process Control
Module # 1.6
Lectures on
CHEMICAL PROCESS CONTROL
Theory and Practice

## Slide 2: A Simple Chemical Process
Recycle A
C
O
L
U
M
N
Product B
REACTOR
A  B
Cooling
Duty
Fresh A
FEHE
ENERGY RECYCLE
MATERIAL RECYCLE
PROCESS INTEGRATION
Minimizes
A consumed per kg B product
Steam consumed per kg B product
ENHANCES PROCESS PROFITABILITY

## Slide 3: Chemical Process Operation
Key Production Objectives
Operate plant to meet production objectives 24X7
Process Disturbances
Production Objective Itself Can Change
Safety
Stability
Economics
Production
Rate
Product
Quality
Effluent
Specs
Ambient
Conditions
Raw material
Quality
Sensor
Noise
Equipment
Characteristics

## Slide 4: Process Control: Basic Objectives
Safety
Stability
≡
Operate Process at Steady State
Accumulation Rate Rate Generation
Rate In Out Rate
=
+
−
Need control system to drive accumulation of all independent inventories to zero
0

## Slide 5: PWC Basics
Regulatory Control System
  Drives all inventory accumulation terms to zero
  Ensures plant operation around a steady state
What steady state to operate at
  Economic Optimum
    Minimize expensive utility consumption
    Maximize production

## Slide 6: Plantwide Control Hierarchy
PLANT
Measurements
Regulatory Control Layer
(updates every few secs)
Supervisory Control Layer
(updates every few mins)
Optimization Layer
(updates every few hrs)
PLANTWIDE CONTROL SYSTEM
SETPOINT
SETPOINT
SIGNAL TO VALVE
Economic Operation
Safe & Stable Operation

## Slide 7: Process Control System Design: Key Issues
Why
  Stabilization (safety and stability)
  Economic optimal operation
What to control
  Independent inventories
  Key indicators that ensure economic operation
    Not a trivial problem (e.g. marathon run vs 100 m sprint)
What to manipulate
  Too many options unlike aero or mech systems
Quantitative algorithms for manipulation
Requires process understanding
Control Theory

## Slide 8: Course Outline
Control Theory
  Material available in all text books
Control Structure Synthesis
  What to control and why
  What to manipulate and why
  Much more obscure
This course covers both aspects in sufficient detail

## Slide 9: Example Cumene Process
Fuel Gas Recovery
Column
Fuel Gas
Recycle
Column
di-isopropyl benzene
Product
Column
Cumene
Recycle benzene
Benzene
Propylene
Preheater
Furnace
Reactor
Cooler
C6H6 + C3H6 → C9H12
C9H12 + C3H6 → C12H18
steam
BFW