## Slide 1: Degrees of Freedom Simple Analysis Procedure
Module # 2.1
Lectures on
CHEMICAL PROCESS CONTROL
Theory and Practice

## Slide 2: Degree of Freedom
What am I free to change
# of variables that can be adjusted (not fixed) INDEPENDENTLY

## Slide 3: Traditional DOF Analysis
DOF =
# of independent variables
#of independent material / energy balances
# of equilibrium constraints
# of specifications
Guaranteed to fail !!!
NEED A SIMPLE AND INTUITIVE METHODOLOGY FOR DOF ANALYSIS

## Slide 4: Liquid Flow Through a Pipe
One adjustable flow
DOF = 1
Liquid Flow Rate
FC

## Slide 5: Liquid Flow Networks
DOF = 3
Three split flows
DOF = 4
Three split flows
One mixed flow
FC
FC
FC
FC
FC
FC
FC

## Slide 6: A Simple Surge Tank
2 adjustable flows
1 level controller
(for material balance)
Control DOF = 2
Dynamic DOF = 1 (Level setpoint)
(Has only dynamic impact. No steady state impact)
Steady operation DOF = 1 (Flow setpoint)
(Sets process throughput)
FC
FC
LC

## Slide 7: Tanks in Series
Control DOF = 5
Steady Operation DOF = 1 (FC: Throughput)
Dynamic DOF = 4 (LCs)
LC
LC
LC
LC
FC

## Slide 8: Heated Flash Drum
Control DOF = 4
Throughput
Heating Rate
Pressure
Level
FC
PC
LC

## Slide 9: Non-Isothermal CSTR
Control DOF = 3
Throughput
Temperature
Level (a SS dof)
FC
TC
LC

## Slide 10: Simple Distillation Column
FC
Control DOF = 6
Throughput
Reboiler Duty or TS
Reflux rate or ratio or TR
Reflux drum level
Bottom Sump Level
Column Pressure
TC
TC
FC
FC
LC
LC
PC

## Slide 11: Packed Bed Reactor
Control DOF = 6
Throughput
Rxr Inlet T
Rxr T
Rxr P
Condensate T
Flash drum level
FC
TC
TC
TC
PC
LC

## Slide 12: A Toy Process
A
B
C
Recycle A, B
A + B → C
Control DOF = 9
Throughput
Rxr Level
Rxr Temperature
Rxr composition
Column L/F
Column Temperature
Column pressure
Reflux drum level
Sump level
LC
LC
LC
X
FC
PC
TC
FC
CC
X
FC
TC

## Slide 13: Discounting Non-Reactive Liquid Levels
FC
FC
LC
Level Must Be Controlled Here
Control DOF 2
Dynamic DOF 1
Steady State DOF 1
Level CANNOT Be Controlled Here
Control DOF 1
Dynamic DOF 0
Steady State DOF 1
FC

## Slide 14: Homogenous Extractive Distillation
FC
Control DOFs 11
LCs 3
Pressures 2
Steady State DOF 6
AB
A
B
Entrainer
X
X
TC
FC
LC
PC
FC
FC
TC
LC
PC
LC
LC

## Slide 15: DOF Exercise: A Petlyuk Column

## Slide 16: The Intuitive DOF Approach
Given a process flowsheet
Show control valve on each adjustable flow
Count # of control valves
Control DOF = # of independent control valves
Steady State
Operation DOF
Control DOF
= - # of non-reactive surge drum level controllers
- any other fixed conditions (e.g. column pressure)