## Slide 1: Dynamic Modelling Approaches
Module 3.1
Lectures on
CHEMICAL PROCESS CONTROL
Theory and Practice

## Slide 2: Dynamic Modelling and Simulation
Essential for process understanding
  Allows tinkering with process inputs
  At worst, a simulation may crash
Allows testing and validating control strategies
  What works and makes sense?
  What does not work and is non-sense?
  Why?
Pushing the envelope
  Superior control algorithms and strategies
Synthesis of area specific knowledge
  Discipline specific do’s and don’ts
Pedagogical resource

## Slide 3: Dynamic Modelling Approaches
Dynamic Process Model
Change MV
Record PV response
Propose simplest combination of basic dynamic elements that fits PV response shape
Best fit basic dynamic element parameters
Develop dynamic model from conservation laws and thermodynamic/other constraints
  Material, energy and momentum balance
  Phase equilibrium, rheology etc
Fit model parameters to plant data
Empirical
First Principles

## Slide 4: Empirical Approach
PARAMETERS
Lag time
Gain
Delay Time
IDENTIFICATION
DESIGN CONTROLLER
VALIDATE PERFORMANCE
Servo & regulator

## Slide 5: The First Principles Approach
A → B
F0, cA0
F, cA
r = k cA
ISOTHERMAL CSTR
ASSUMPTIONS
Isothermal
Well mixed
Fixed volume
A component balance
NON-ISOTHERMAL CSTR
ASSUMPTIONS
Well mixed reactor
Well mixed jacket
Fixed volume
Constant CP ρ U -ΔHrxn
Arrhenius rate constant
A component balance
Reactor energy balance
A → B
F0, cA0, T0
F, cA, T
r = k cA
TJ
Total material balance
F0 = F at all times
Total material balance
F0 = F at all times
Process
F0
cA0
F
cA
COUPLED NON-LINEAR ODES WITH ALGEBRAIC CONSTRAINTS
Solve numerically
Linearize and solve analytically (not guaranteed)
cA
Process
F0
cA0
F
T0
T
TJ

## Slide 6: The First Principles Approach
Develop process model equations
  Realistic assumptions
  Dynamic balances
    Material, energy, component or momentum balances
  Process constraints
    Phase equilibrium (equal fugacity), thermal equilibrium, given specifications etc
  Relevant material properties
    Thermodynamics: Enthalpy, specific heat, heat of reaction, activity coefficients etc
    Kinetics: Reaction rate expressions and parameters
    Constitutive: Viscosity expression
Develop numerical procedure for solving system of DAEs
Simulate, test and validate process model (including parameter fitting)
Apply control system equations on top of process model
Simulate, test and validate process control performance

## Slide 7: Dynamic Modelling Approaches
Dynamic Process Model
Change MV
Record PV response
Propose simplest combination of basic dynamic elements that fits PV response shape
Best fit basic dynamic element parameters
Develop dynamic model from conservation laws and thermodynamic/other constraints
  Material, energy and momentum balance
  Phase equilibrium, rheology etc
Fit model parameters to plant data
System of linear ODEs
Elegant analytical solutions
Well established theory
System of non-linear DAEs
Solved numerically
May get analytical solutions by linearization
Theory under development. Too complex
Very practical and simple
Applies in vicinity of MV-PV response test
Empirical
First Principles
Complex (including plant testing & fitting)
Applies to a wider operating range
Helps develop process understanding

## Slide 8: Summary
Dynamic process models essential for control studies
  Empirical
  First Principles
Empirical Approach
  Simple and practical
  Applies ‘locally’
  Analytical solutions
  Well established linear control theory
First principles approach
  Apply material and energy balances
  Non-linear models
  Capable of describing process behavior over a large operating space
  Realistic but complex
  Usually solved numerically
  Effect of principal disturbances can be modeled
  Develops process understanding