## Slide 1: Dynamic Modelling First Principles Models Complex Systems
Module 3.3.2
Lectures on
CHEMICAL PROCESS CONTROL
Theory and Practice

## Slide 2: Multicomponent Flash Drum
PC
LC
FC
TC
F
TF PF z
PRV
Given F TF PF z & P
Build steady state & dynamic model of flash drum
ASSUMPTIONS
Negligible vapour hold up
Instantaneous vapour dynamics (perfect PC)
Negligible ambient losses
TV = TL = T (thermal equilibrium)
PV = PL = P
Vapor liquid equilibrium
Constant molar heat capacity and latent heat
STEADY STATE DOF ANALYSIS
# of variables 3(C+2)
Material balances C
Energy balance 1
VLE constraints C
Given feed conditions C+2
Specified drum pressure 1
TV = TL 1
PV = PL 1
3C+2

## Slide 3: Flash Drum: Steady State Solution
MATERIAL BALANCE
VAPOR LIQUID EQUILIBRIUM
ENERGY BALANCE
Read F z TF PF P
Guess T
Perform TP flash to get
V, x, y
Obtain VEB from energy balance
Is |V-VEB| < tol
Stop
Yes
No

## Slide 4: Flash Drum: Dynamic Simulation
DYNAMIC MATERIAL BALANCE
VAPOR LIQUID EQUILIBRIUM
ENERGY BALANCE
Obtain initial steady state solution
Is t > tend
Stop
Yes
CONTROLLER EQUATION
Initialize N(0) t = 0
Read F(t) z(t) TF(t) PF(t)
BubbleT Calculation at t
Gives [T(t), y(t)] given (P, x(t))
Obtain L(t) from controller equation
Integrate forward material balances
No
t = t + Δt

## Slide 5: Flash Drum Simulation
Benzene-Toluene-Xylene Flash
1 kmol/min
Equimolar
200 °C
100 kPa
107.61 °C
[0.2226 0.3433 0.4340]
[0.4902 0.3192 0.1906]
0.4196 kmol/h
0.5864 kmol/h
Nominal Steady State

## Slide 6: Summary
Non-linear DAEs usually describe dynamics of realistic process systems
Linearization is usually not possible for such systems
Realistic systems must be solved numerically
Commercial simulators (Aspen Plus Hysys)perform the numerical calculations
  Obtaining steady state solution
  Dynamics around the steady state