## Slide 1: Laplace Domain Analysis The Transfer Function
Module 4.2
Lectures on
CHEMICAL PROCESS CONTROL
Theory and Practice

## Slide 2: The Transfer Function
Compact Laplace domain representation of LTI-ODE (0 ICs)
General Form
Factorize numerator and denominator
ZEROES of G
POLES of G
G
u
y
BLOCK DIAGRAM

## Slide 3: The Transfer Function
Time Domain ODE
Laplace Domain Transfer Function
Transfer Function
Denominator
Polynomial
ODE
Characteristic Equation
Polynomial
≡
POLES OF THE TRANSFER FUNCTION ARE THE ROOTS OF THE ODE CHARACTERISTIC EQUATION

## Slide 4: Nature of Forced LTI-ODE Solution
G
u
y
G has v distinct real poles, w complex conjugate pair poles and q repeated real poles with the kth repeated pole (k = 1 to q) repeated rk times
Then
Using partial fractions
Reverting back to time domain

## Slide 5: Poles and Transient Response
G
u
y
Poles, p, determine the ept terms (eigenfunctions) in transient response
Poles may be real (distinct or repeated) or complex conjugate
Imaginary part in complex conjugate pairs results in oscillations
If real part of pole is negative, corresponding eigenfunction decays with time
If real part of pole is positive, corresponding eigenfunction blows up with time
If all poles in LHP, system is stable
If any pole in RHP, system is unstable

## Slide 6: System Stability
S or λ plane
Re
Im
LEFT HALF PLANE
STABLE
RIGHT HALF PLANE
UNSTABLE
If ANY transfer function pole (characteristic equation root) is in RHP, system is UNSTABLE
Only if ALL transfer function poles (characteristic equation roots) are in LHP, system is STABLE

## Slide 7: Pole Location and Corresponding Transients
Frequency
of
oscillation
=
Complex part
of
pole

## Slide 8: Pole Location and Transient Response Speed
S or λ plane
Re
Im

## Slide 9: Zeroes and Transient Response
G
u
y
Zeroes, z, affect the partial fraction coefficients
Zeroes affect the dynamic response through the coefficients
RHP zero causes inverse response
Zeroes have no role in determining the eigenfunctions (transient modes)

## Slide 10: Pole-Zero Map & Dominant Poles
S or λ plane
Re
Im
All poles in LHP Stable system
For a stable system, pole closest to the RHP has the slowest transient
It dominates the
transient response
If other poles are sufficiently away from dominant pole,
Transient response ≈ Response due to dominant poles
DOMINANT POLE APPROXIMATION
KEY FEEDBACK CONTROL IDEA
Tune controller such that dominant closed loop pole is sufficiently away from RHP
Typical criteria 0 < ξ < 0.5
cos-1ξ
In a feedback control loop, some of the closed loop poles move towards RHP as KC is increased

## Slide 11: Summary
Transfer function
  Implicitly assumes 0 ICs
  Compact ODE representation in Laplace domain
  Numerator polynomial (roots are zeroes) and denominator polynomial (roots are poles)
Transfer function zeroes
  Affect transient response by affecting the partial fraction coefficients
Transfer Function Poles
  Are the roots of the ODE characteristic equation
  May be real distinct, real repeated or complex conjugate pairs
  Determine the eigenfunctions (ept terms) in the transient response
  Transient response is linear combination of eigenfunctions
  Complex conjugate roots cause sinusoidal oscillations of frequency = imaginary part
  System is stable if all poles in LHP. Else unstable
Dominant pole
  In a stable system, pole closest to RHP dominates the transient response
  Feedback controller tuned s.t. dominant closed loop pole sufficiently way from RHP