## Slide 1: Laplace Domain Analysis Block Diagrams for Process Systems
Module 4.4
Lectures on
CHEMICAL PROCESS CONTROL
Theory and Practice

## Slide 2: Non-Isothermal CSTR
A → B
F0 cA0 T0
F cA T
r = k cA
TJ
Block diagram for effect of T0 on T and cA
EXERCISE
Block diagrams for effect of
cA0, F0 or TJ on T and cA

## Slide 3: Exothermic Reactor-FEHE
Reactor
FEHE
T0
T1
T2
T3
Block diagram for effect of T0 on T2
RECYCLE EFFECT
Much higher gain
Much larger time constant (ie slow dynamics)
Possible instability if K12K21 > 1

## Slide 4: Distillation Column
V, y1
L, x
Block diagram for effect of L on y1
EXERCISE
Derive transfer function relating y1 and L

## Slide 5: Summary
Physical process structure determines the block diagram structure
CSTR example
  Coupled material and energy balance
Reactor FEHE example
  Energy recycle causes large increase in process gain and time constant
  Process may become unstable
Distillation column example
  Interacting lags in series