## Slide 1: Laplace Domain Analysis SISO Feedback Loops Analysis and Design
Module 4.4
Lectures on
CHEMICAL PROCESS CONTROL
Theory and Practice

## Slide 2: SISO Feedback Loop
Gp
Σ
Gd
u
d
y
Gc
Σ
ySP
-1
e
y
Σ
d
ySP
Servo tf
Regulator tf
CLOSED LOOP CHARACTERISTIC EQUATION
1 + GpGc = 0
PID Controller

## Slide 3: PID Controller: Analysis and Design
ANALYSIS
Given a dynamic system, what are its dynamic response characteristics
DESIGN
For desired closed loop response characteristics, obtain controller tuning (Kc, τI and τD)
Metrics Characterizing Closed Loop Response
Time Domain:
Rise time, peak time, POR, DR
Laplace Domain:
Closed loop damping coefficient (ξ) of dominant pole-pair

## Slide 4: Is the System Stable?
Governed by system characteristic equation roots (transfer function poles)
  If any root / pole in RHP, system is unstable
  If all roots in LHP, system is stable
Need a simple technique for # of RHP poles
  Without calculating all roots
Routh array is that simple technique
  Write down characteristic equation p(s) = 0
  Prepare Routh array of p(s)
  # of RHP roots = # of sign changes in first column of Routh array
For closed loop systems, Routh array may be used to calculate limiting KC at which system goes unstable

## Slide 5: The Routh Array
General Characteristic Equation
Power | Coefficients |  |  |  | 
 |  |  |  |  | Odd/even coefs
 |  |  |  |  | Even/odd coefs
Power | Coefficients |  |  |  | 
 |  |  |  |  | Odd/even coefs
 |  |  |  |  | Even/odd coefs
# of RHP roots/poles = # of sign changes in first column of Routh array

## Slide 6: Routh Array: Special Cases
Common factor in a row
  Divide all elements by the common factor
Zero first element in a row
  Replace 0 by infinitesimal δ and complete array
  Look at signs of elements above and below δ
    If same sign, then a purely imaginary conjugate root pair is indicated
    If sign change, # of sign changes = # of RHP roots
  Alternatively, replace s by x-1 and obtain Routh array for revised p(x) = 0
Entire row is zero
  Replace zero row by coefficients of d/ds[Auxiliary Polynomial] and proceed
  Auxiliary polynomial = polynomial for row above zero row
  Indicates complex conjugate root pairs or (+a, -a) root pairs
  Auxiliary polynomial always of even degree
  Roots of auxiliary polynomial give conjugate/(+a,-a) roots pairs

## Slide 7: Routh Array Example 1
ROUTH ARRAY
s5 120 (8) 225 (15) 15 (1) common factor 15
s4 274 85 3
s3 12.52 0.912 0
s2 65 3
s1 0.335 0
s0 3
0 sign changes in first column 0 RHP roots Stable system

## Slide 8: Routh Array Example 2
ROUTH ARRAY
s5 120 (8) 225 (15) 15 (1) common factor 15
s4 274 85 5
s3 12.52 0.8540 0
s2 66.31 5
s1 -0.09 0
s0 5
2 sign changes in first column 2 RHP roots Unstable system

## Slide 9: Routh Array Example 3
ROUTH ARRAY
s5 120 (8) 225 (15) 15 (1) common factor 15
s4 274 85 4.571
s3 12.52 0.8665 0
s2 66.03 4.571
s1 δ 0
s0 4.571
Purely imaginary root pair corresponds to 66.03s2 + 4.571 = 0 s = ± 0.2631j
No RHP root. 2 purely imaginary root pair System with sustained oscillations

## Slide 10: Routh Array Example 4
ROUTH ARRAY
s5 1 3 -4
s4 3 (1) 9 (3) -12 (-4) Common factor 3
s3 0 (4) (2) 0 (6) (3) Aux polynominal. 2 common
s2 1.5 -4
s1 8.33
s0 -4
1 sign changes in first column 1 RHP root Unstable system
Aux poly: s4 + 3s2 – 4 = 0 s = ±2j & s = ±1 are roots of p(s) = 0. Remaining root s = -3
p(s) ≡ (s+1)(s-1)(s+2j)(s-2j)(s+3)

## Slide 11: Routh Array Example 5
Consider SISO system with
It is controlled using a P only controller. Use Routh array to
Obtain controller gain range for which closed loop system is stable
Frequency of oscillations at the verge of instability
ROUTH ARRAY
s5 120 (8) 225 (15) 15 (1) common factor 15
s4 274 85 α
s3 b=12.52 c=1-0.0292α
s2 d=63.112+0.6391α α
s1 e 0
s0 α
For no sign change, α = 1+5KC < 4.5710 KC < 0.714
At α = 4.57, aux. poly. ≡ ds2 + α = 0 66.0327s2 + 4.570 = 0 s = ±0.2631j
Frequency of oscillation at verge of instability 0.2631 rad/min
Routh Array Example 5

## Slide 12: Ultimate Gain and Period
Ultimate gain (KU)
  Proportional controller gain for which sustained closed loop oscillations occur
Ultimate period (PU)
  Sustained oscillation period at KU
KU, PU used for empirical tuning

## Slide 13: Empirical Tuning Rules
Give KC, τI and τD in terms of KU and PU
  Experience based tuning rules (empirical)
Zeigler-Nichols
  Developed for quarter decay ratio regulator response in typical systems
  Aggressive
  Use when aggressive control is desired (e.g. exothermic reactor T control)
Tyreus-Luyben
  Used on most process systems for gentle changes in MVs (smooth operation)

## Slide 14: Empirical Tuning Rules
ZIEGLER-NICHOLS |  |  | 
Controller | KC | τI | τD
P only | KU/2 | - | -
PI | KU/2.2 | PU/1.2 | -
PID | KU/1.7 | PU/2 | PU/8
TYREUS-LUYBEN |  |  | 
Controller | KC | τI | τD
PI | KU/3.2 | 2.2PU | -
PID | KU/2.2 | 2.2PU | PU/6.3
CIANCONE-MARLIN |  |  | 
Controller | KC | τI | τD
PI | KU/3.3 | PU/4 | -
PID | KU/3.3 | PU/4.4 | PU/8.1
Lag Dominant
Delay Dominant

## Slide 15: Example 1
Consider a SISO process with
Calculate KU, PU and ZN settings for P, PI and PID controllers
At KC = KU, s = jω satisfies CLCE
ZIEGLER-NICHOLS |  |  | 
Controller | KC | τI (min) | τD (min)
P only | 2.81 | - | -
PI | 2.56 | 2.80 | -
PID | 3.31 | 1.68 | 0.42

## Slide 16: Example 2
Consider a SISO process with
Tune a P controller for a closed loop damping coefficient of 0.7071 (1/sqrt(2))
For s = -a + aj satisfies CLCE
Kc = 0.3369

## Slide 17: Example 3
Consider a SISO process with
Tune a PI controller KC for a closed loop damping coefficient of 0.7071 (1/sqrt(2)). τI is chosen to cancel the dominant open loop pole.
For s = -a + aj satisfies CLCE
Kc = 0.3262

## Slide 18: Example 4
Consider a SISO process with
Tune a PID controller KC for a closed loop damping coefficient of 0.7071 (1/sqrt(2)). τI and τD are chosen to cancel the slowest and fastest open loop poles, respectively.
For s = -a + aj satisfies CLCE
Kc = 0.4759

## Slide 19: Dynamic Responses

## Slide 20: Summary
Dynamic System Analysis vs Design for Dynamic Performance Spec
Routh Array
  A simple tool for determining system stability
  Controller tuning limit(s) for system stability
Ultimate gain and Ultimate period
  Correspond to P controller gain at verge of instability
  Used in empirical tuning rules for PID tuning
Controller design
  KC adjusted so that dominant closed loop pole pair has desired ξ
  Governed by closed loop characteristic equation