## Slide 1: Laplace Domain Analysis Root Locus Construction Rules
Module 4.6.1
Lectures on
CHEMICAL PROCESS CONTROL
Theory and Practice

## Slide 2: Root Locus
Locus of closed loop characteristic equation roots as controller gain magnitude |KC| is varied from 0 to ∞
Gp
Σ
Gd
u
d
y
Gc
Σ
ySP
-1
e
CLCE

## Slide 3: Root Locus: Angle Condition
Gp
Σ
Gd
u
d
y
Gc
Σ
ySP
-1
e
CLCE
s is a complex number in general.
G(s) is therefore a complex number in general.
CLCE is satisfied for those special values of s for which G(s) is a negative real number i.e.
ANGLE CONDITION
Those special values of s are on the root locus for which is odd multiple of π

## Slide 4: s-plane and G-plane Mapping

## Slide 5: Locus Construction Rules
RULE 1 Locus has n branches
RULE 2 Loci begin at n open loop poles
RULE 3 Loci end at m open loop zeroes and n-m asymptotes
RULE 4 Root locus is symmetric about real axis

## Slide 6: Locus Construction Rules
RULE 5 Locus on real axis
Locus exists on real axis is # of poles and zeroes to right is odd
Locus does not exist on real axis if # of poles and zeroes to right is even

## Slide 7: Locus Construction Rules
RULE 6 Angle of asymptotes

## Slide 8: Locus Construction Rules
RULE 7 Real axis intercept (σ) of asymptotes

## Slide 9: Locus Construction Rules
RULE 8 Locus break-out and break-in points on real axis
At break-out (break-in) point (i.e. CLCE has repeated real roots), |G(s)| is maximum (minimum)

## Slide 10: Locus Construction Rules
RULE 9 Angle of departure from complex pole
Angle of departure is 180° - angle subtended by other poles + angle subtended by other zeroes
RULE 10 Angle of arrival at complex zero
Angle of arrival is 180° + angle subtended by other poles - angle subtended by other zeroes

## Slide 11: Locus Construction Rules
RULE 11 Angle condition in vicinity of break-out (in) point

## Slide 12: Locus Construction Rules
RULE 12 Conservation of roots
If n – m ≥ 2, then sum of CLCE roots = sum of open loop poles

## Slide 13: Construction Rules’ Summary
RULE 1 Locus has n branches
RULE 2 Loci begin at n open loop poles
RULE 3 Loci end at m open loop zeroes and n-m asymptotes
RULE 4 Root locus is symmetric about real axis
RULE 5 Locus exists on real axis only if # of poles and zeroes to right is odd
RULE 6
RULE 7 Real axis intercept of asymptotes
RULE 8 At break-out (break-in) point, |G(s)| is maximum (minimum) a – b
RULE 9 (10) Angle of departure (arrival) from (to) complex zero = 180° – (+) other poles + (–) other zeroes
RULE 11 Angle condition in vicinity of break-out (in) point allows iterative calculation of the point
RULE 12 Conservation of CLCE roots. If n – m ≥ 2, then sum of CLCE roots = sum of open loop poles