## Slide 1: Plantwide Control Fundamentals
Process Dynamics and Control
Supplementary Material
Indian Institute of Technology Kanpur
Module # 7.1

## Slide 2: PWC Basics: A Simple Chemical Process
Recycle A
C
O
L
U
M
N
Product B
REACTOR
A  B
Cooling
Duty
Fresh A
FEHE
ENERGY RECYCLE
MATERIAL RECYCLE
PROCESS INTEGRATION
Minimizes
A consumed per kg B product
Steam consumed per kg B product
ENHANCES PROCESS PROFITABILITY

## Slide 3: PWC Basics: Chemical Process Operation
Key Production Objectives
Operate plant to meet production objectives 24X7
Process Disturbances
Production Objective Itself Can Change
Safety
Stability
Economics
Production
Rate
Product
Quality
Effluent
Specs
Ambient
Conditions
Raw material
Quality
Sensor
Noise
Equipment
Characteristics

## Slide 4: PWC Basics
Safety
Stability
≡
Operate Process at Steady State
Accumulation Rate Rate Generation
Rate In Out Rate
=
+
−
Need PWC to drive accumulation of all independent inventories to zero
0

## Slide 5: PWC Basics
Regulatory Control System
  Drives all inventory accumulation terms to zero
  Ensures plant operation around a steady state
What steady state to operate at
  Economic Optimum
    Minimize expensive utility consumption
    Maximize production

## Slide 6: Plantwide Control Hierarchy
PLANT
Measurements
Regulatory Control Layer
(updates every few secs)
Supervisory Control Layer
(updates every few mins)
Optimization Layer
(updates every few hrs)
PLANTWIDE CONTROL SYSTEM
SETPOINT
SETPOINT
SIGNAL TO VALVE
Economic Operation
Safe & Stable Operation

## Slide 7: Regulatory PWCS Design
What to Control
  All independent inventories (DOF)
    Material – Liquid level or gas pressure
    Energy – Temperature or vapor pressure
    Component – Composition, tray temperature (inferential)
  Throughput or Production Rate
Degree of tightness of control
  Should energy inventories be tightly controlled?
  Should surge level inventories be tightly controlled?
What to manipulate
  The largest term on the RHS of the inventory balance
    Richardson’s Rule
  Pair close
    Fast dynamics
    Tight closed loop control

## Slide 8: Control Structure Alternatives
REACTOR
A  B
Cooling
Water
Fresh A
Recycle A
C
O
L
U
M
N
Product B
FC
TC
LC
PC
LC
LC
RC
TC
TPM

## Slide 9: Alternative Control Structures
REACTOR
A  B
Cooling
Water
Fresh A
Recycle A
C
O
L
U
M
N
Product B
TC
LC
PC
LC
LC
RC
TC
TPM
FC
Alternative Control Structures

## Slide 10: Alternative Control Structures
REACTOR
A  B
Cooling
Water
Fresh A
Recycle A
C
O
L
U
M
N
Product B
TC
PC
LC
RC
TC
TPM
FC
LC
LC

## Slide 11: Alternative Control Structures
REACTOR
A  B
Cooling
Water
Fresh A
Recycle A
C
O
L
U
M
N
Product B
TC
PC
LC
LC
RC
TC
LC
TPM
FC

## Slide 12: Alternative Control Structures
REACTOR
A  B
Cooling
Water
Fresh A
Recycle A
C
O
L
U
M
N
Product B
TC
PC
LC
RC
LC
TC
LC
TPM
FC

## Slide 13: Alternative Control Structures
REACTOR
A  B
Cooling
Water
Fresh A
Recycle A
C
O
L
U
M
N
Product B
RC
TC
PC
LC
TC
LC
LC
TPM
FC

## Slide 14: PWCS Design: Key Points
Location of through-put manipulator a key decision for inventory management
Several alternative ‘reasonable’ plant-wide control structures
Which one is the ‘best’
How do you bring method to the madness

## Slide 15: The Transformation of Variability Perspective
HEAT EXCHANGER EXAMPLE
Condensate out
Process Stream in
HEAT EXCHANGER
Steam in
Control
Valve
Process Stream out
Transmitter
TC
TT
Steam Flow
Temperature
Steam Flow
Temperature
CONTROL
SYSTEM
Agent for transformation / management of process variability

## Slide 16: Where to Transform Variability
Surge level
  Does not affect steady state
  Regulate loosely for filtering out flow transients
Energy Inventories
  Regulate tightly to guarantee safety (rxn runaway?)
Product quality
  Regulate tightly
  Minimize “free” product give-away
Production rate
  Often “loose” is OK (eg meet the monthly target)
Recycle loop circulation rates
  Regulate tightly
  All equipment inside recycle loop see low variability
  May need to let it float for overall balance closure

## Slide 17: A Common Energy Recycle Loop
T0↑
REACTOR
FEHE
Feed
TR
TE
QFEHE
QHtr≠0
QCool
TC
PC
FC
TPM
LC
TC
TR
Temperature controller transforms energy balance variability out of recycle loop
Regulates energy recycled in FEHE

## Slide 18: A Common Energy Recycle Loop continued
T0↑
REACTOR
FEHE
Feed
TR
TE
QFEHE
QHtr=0
QCool
TC
FC
TPM
LC
TC
TR
TC
0%
PC
Temperature controller transforms energy balance variability out of recycle loop
Regulates energy recycled in FEHE

## Slide 19: Material Recycle Snowball Effect
REACTOR
A  B
Cooling
Water
Fresh A
Recycle A
C
O
L
U
M
N
Product B
TC
LC
PC
LC
LC
RC
TC
FC
TPM
Time
%
FA
R
Recycle loop shows large swings
Large Throughput De-rating

## Slide 20: Material Recycle Snowball Effect continued
REACTOR
A  B
Cooling
Water
Fresh A
Recycle A
C
O
L
U
M
N
Product B
TC
LC
PC
LC
LC
RC
TC
FC
TPM
No large swings in recycle rate
Lower Throughput De-rating

## Slide 21: Key Guideline for Recycle Loops
Structure the control system to transform variability out of the recycle loop
  Hold what’s going around the recycle loop
Energy Recycle Loop
  Hold a temperature inside the recycle loop
Material Recycle Loop
  Hold component rate(s) going around recycle loop
  Material balance control structure brings in fresh component(s) that are recycled as make-up streams