## Slide 1: Plantwide Control Fundamentals Economic Operation
Process Dynamics and Control
Supplementary Material
Indian Institute of Technology Kanpur
Module # 7.4

## Slide 2: PWC Basics
Regulatory Control System
  Drives all inventory accumulation terms to zero
  Ensures plant operation around a steady state
What steady state to operate at
  Economic Optimum
    Minimize expensive utility consumption
    Maximize production

## Slide 3: Plantwide Control Hierarchy
PLANT
Measurements
Regulatory Control Layer
(updates every few secs)
Supervisory Control Layer
(updates every few mins)
Optimization Layer
(updates every few hrs)
PLANTWIDE CONTROL SYSTEM
SETPOINT
SETPOINT
SIGNAL TO VALVE
Economic Operation
Safe & Stable Operation

## Slide 4: Regulatory PWCS Design
What to Control
  Throughput or Production Rate (TPM selection)
  All independent inventories (DOF)
    Material – Liquid level or gas pressure
    Energy – Temperature or vapor pressure
    Component – Composition, tray temperature (inferential)
Degree of tightness of control
  Energy inventories should be tightly controlled.
  Surge level inventories should be loosely controlled.
What to manipulate
  The largest term on the RHS of the inventory balance
    Richardson’s Rule
  Pair close
    Fast dynamics
    Tight closed loop control

## Slide 5: PWC Basics: TPM Selection
When is TPM choice flexible
  Large storage tanks supply the fresh feed(s)
  Variability in storage tank level is acceptable
    Allows structures that bring in fresh feed(s) as make-up
Usually plant designs have large recycle rates
  Design in the snowballing region
  Capacity bottleneck then is likely inside the loop
Where to locate the TPM
  Inside the recycle loop
  If multiple recycle loops, on a common branch
  If bottleneck is known, AT the bottleneck

## Slide 6: Key PWC Guidelines
Configure control structure to transform recycle rate variability out of the recycle loop
Provide control DOFs for fast “local” control
“Pair” locally for fast control
Choose TPM at bottleneck constraint to transform variability away from bottleneck
  Almost always, bottleneck is inside the recycle loop

## Slide 7: Economic Operation Considerations
J
u
uMIN
uMAX
J
u
uMIN
uMAX
J
u
uMIN
uMAX
Operate at uMAX always
Operate at uMIN always
uopt
Operate at uopt
uopt changes
Loss
ECONOMIC OBJECTIVE
MINIMIZE J over dofs u
subject to process contraints

## Slide 8: The “What to Control” Paradigm
J
u
uMIN
uMAX
Optimum remains “nearly” the same
Find those “magic” process variables with invariant optimum
WHAT TO CONTROL
All active constraints
Economic CVs

## Slide 9: Optimal Operating Policy Example
100 m Sprint
100%
40 km Marathon
Image taken from: https://www.vectorstock.com
Constant Speed
Constant Breathing Rate
J = minu Race Completion Time
Running Effort
Running Effort
Constant Effort
J = minu Race Completion Time
Speed SP
SC
BR SP
BRC
NEED PROCESS INSIGHT FOR DEVELOPING OPTIMAL OPERATING POLICY
The Skogestad Example

## Slide 10: PWCS Design Steps
DOF analysis and control objectives
  Production rate
  Product quality
  Safety limits (eg UFL < gas loop composition < LFL)
  Economic
Choose TPM
  Feed set by an upstream process
  On demand operation (utility plants)
  Flexible
    Inside the recycle loop at the feed of the most non-linear/fragile unit
    If bottleneck is known, at the bottleneck inside the recycle loop
Design “local” loops for closing all independent material and energy balances around the TPM
  Radiate outwards from the TPM
  Check consistency of material / energy balance closure (Downs’ Drill)
Choose loop setpoints “wisely”
  Usually governed by economic considerations

## Slide 11: Reactor-Separator-Recycle Process
A + B → C
FA
FB
E
R, xCR
P, xCP
KM I
KM II:
KM III:
KM IV:
DOF ANALYSIS
Control DOFs 9
Surge levels 2
Given Column P 1
Steady State DOF 6
Production rate P
Product purity xCP MIN
Max reactor Temperature TrxrMAX
Max reactor Holdup VrxrMAX
Max recycle impurity xCR MAX
Unconstrained DOF 1

## Slide 12: Mode I Economic Operation
At given production rate, P
Find the globally optimal control law for 1 unconstrained DOF that
minimizes recycle rate, R
R is surrogate for column boilup

## Slide 13: Mode I Optimal Invariant: KM I
A + B → C
FA
FB
E
R, xCR
P, xCP
CONSTRAINTS
1. Overall Material Balance
2. Column Unreacted Reactants (A+B) Balance
OPTIMALITY CONDITION
MINIMIZE R at given production, P
2 =>
d/dxB
1 =>
d/dxB
0
KM I:

## Slide 14: Mode II Optimal Invariant: KM I
A + B → C
FA
FB
E
R, xCR
P, xCP
KM I:
CONSTRAINTS
1. Overall Material Balance
2. Column Unreacted Reactants (A+B) Balance
OPTIMALITY CONDITION
Maximize P subject to bottleneck RMAX
2 =>
d/dxB
0
1 =>
d/dxB
0

## Slide 15: Interpretation
A + B → C
FA
FB
E
R, xCR
P, xCP
KM I:
MODE I
Minimum R Minimize unreacted reactant in rxr
Min xA + xB
MODE II
Maximum P Maximize C mol fr in rxr, xC
Max 1-xA-xB

## Slide 16: Optimal Invariants
Kinetic Model | Mode I Invariant | Mode II Invariant
KM I (Elementary) |  | 
KM II (Power Law) |  | 
KM III (LH) |  | 
KM IV (LH-Power Law) |  | 
Kinetic Model | Mode I Invariant | Mode II Invariant
KM I (Elementary) |  | 
KM II (Power Law) |  | 
KM III (LH) |  | 
KM IV (LH-Power Law) |  | 
ECONOMIC CV

## Slide 17: Practical Case
Mode I
  Minimize boilup or reboiler duty at given production
  Recycle rate and boilup correlated but not linearly related
Mode II
  Maximize production subject to maximum boilup as bottleneck
  Bottleneck corresponds to column flooding
Candidate economic CVs
  Reactor B mol fr, xB
  Reactor A/B ratio, xA/xB
  Global invariant (RHS – LHS = 0)

## Slide 18: Economic Performance Quantification
── : [A/B] at nominal optimum
- - - : xrxrB at nominal optimum
KM I
KM II
KM III
KM IV
Mode I
Mode II

## Slide 19: Economic Performance Quantification
Mode I
Mode II
Constant reactor A/B ratio a good economic CV for all reaction kinetic types

## Slide 20: Inferring Reactor A/B Ratio
A + B → C
FA
FB
E
R, xCR
P, xCP
Hold reactor A/B constant
Ttop
Ttop infers reactor A/B ratio

## Slide 21: Ttop as Economic CV
Mode I
Mode II
Ttop is a good economic CV

## Slide 22: Plantwide Control Structure, CS1
A + B → C
FA
FB
E
R, xCR
P, xCP
TC
FC
LS
VMAX
TPM
LC
TC
LC
PC
LC
FC
X
FC
CC
xCR MAX
CC
xB
Trxr MAX
LVLrxr MAX
CC
xCP MIN
Economic CV: xB

## Slide 23: Plantwide Control Structure, CS 2
A + B → C
FA
FB
E
R, xCR
P, xCP
TC
FC
LS
VMAX
TPM
LC
TC
LC
PC
LC
FC
X
FC
CC
xCR MAX
Trxr MAX
LVLrxr MAX
CC
xCP MIN
TC
Ttop
Economic CV: Ttop

## Slide 24: Mode I Throughput Change Response
CS1: xB constant
CS2: Ttop constant
+20% Throughput: CS1 boilup ~7.0% higher -20% Throughput: CS1 boilup ~3.6% higher

## Slide 25: Mode I Catalyst Deactivation Response
CS1: xB constant
CS2: Ttop constant
20% Deactivation: CS1 boilup ~12% higher

## Slide 26: Mode II Catalyst Deactivation Response
CS1: xB constant
CS2: Ttop constant
30% Deactivation: CS1 production ~0.8% lower

## Slide 27: Summary
What to control holds the key to effective plantwide control
  Control all active constraints
  Control SOCVs for unconstrained dofs
Proper choice of TPM (inside the recycle loop) ensures robust regulation
  Significant max throughput benefit (up to 25% in ester process example)
Self-optimizing CVs for unconstrained variables can result in significant energy savings
  7-12% energy savings in example reactor-separator recycle process
Presented approach provides method to the madness that plantwide control can be