## Slide 1: Plantwide Control Fundamentals Cumene Process PWCS Design
Process Dynamics and Control
Supplementary Material
Indian Institute of Technology Kanpur
Lecture # 7.5

## Slide 2: Cumene Process
Vaporizer
FEHE
Furnace
Product
C9
C12
Alkylation
C3 + C6 → C9
C9 + C3 → C12
Vent
Purge
Recycle C6
C6
C3
Recycle
Transalkylation
C12 + C6 ↔ 2C9
Transalkylator
Alkylator

## Slide 3: DOF Analysis
Vaporizer
FEHE
Furnace
Product
C9
C12
Vent
Purge
Recycle C6
C6
C3
Recycle
Transalkylator
Alkylator
# of Control Valves 25
# of LCs 8
Given Column Ps 3
Given Reactor P 1
STEADY STATE DOF 13

## Slide 4: Steady State Specifications
Production Rate (Throughput)
C6 Impurity in Product
C9 Impurity in Product
Reactor Feed Temperature
Reactor Temperature
Purge Column Top Temperature
C3 Impurity in Purge Column Bottoms
Specified Variable | Comment 1 | Comment 2
Throughput (Production Rate) | Specified by business side | First fresh feed DoF
Main reactor C6 to C3= ratio | Excess C6 to suppress C12 formation | Second fresh feed DoF
C6 Impurity in Product | Fixed by product quality requirement | Recycle column DoF 1 (bottom LK impurity)
C12 Impurity in Product | Fixed by product quality requirement | Product column DoF 1 (top HK impurity)
Reactor Feed Temperature | Set by furnace duty | Furnace DoF
Reactor Temperature | Set by reactor cooling duty | Reactor DoF
Purge Column Top Temperature | ~ 50 °C. Set by condenser cooling water | Purge column DoF 1
Purge Column Bottom C3 Impurity | Set to a small value (say 0.1 mol%) | Purge column DoF 2
Recycle Column Top C9 Impurity | Set to a small value (say 0.1 mol%) | Recycle column DoF 2 (top HK impurity)
Product Column Bottom C9 Impurity | Set to a small value (say 1 mol%) | Product column DoF 2 (bottom LK impurity)
TA reactor inlet temperature | Set by TA preheater | TA preheater DoF
TA effluent cooler outlet temperature | Set by TA effluent cooling duty | TA effluent cooler DoF
TA C6 to C12 ratio | High value (shifts equilibrium to right) | C6 recycle splitter DoF
Flash Drum Cooler Sets Reactor Pressure

## Slide 5: Conventional PWCS: TPM at C3 Feed
Vaporizer
FEHE
Furnace
Product
C9
C12
Alkylation
C3 + C6 → C9
C9 + C3 → C12
Vent
Purge
Recycle C6
C6
C3
Recycle
Transalkylation
C9 + C6 ↔ C9
Transalkylator
Alkylator
FC
TPM
LC
TC
TC
LC
PC
LC
PC
LC
LC
LC
PC
LC
LC
PC
TC
TC
TC
TC
FC
X
FC
X
TC
TC
FC
FC
X
X
CC
CC

## Slide 6: Bottleneck: Recycle Column Flooding
Vaporizer
FEHE
Furnace
Product
C9
C12
Alkylation
C3 + C6 → C9
C9 + C3 → C12
Vent
Purge
Recycle C6
C6
C3
Recycle
Transalkylation
C9 + C6 ↔ C9
Alkylator
FC
LC
LC
LC
TC
Transalkylator
TC
PC
LC
TC
TC
TC
TC
PC
LC
LC
PC
LC
LC
PC
TC
TC
FC
X
FC
X
FC
FC
X
X
CC
CC
FC
TPM

## Slide 7: Bottleneck: Furnace Duty
Vaporizer
FEHE
Furnace
Product
C9
C12
Alkylation
C3 + C6 → C9
C9 + C3 → C12
Vent
Purge
Recycle C6
C6
C3
Recycle
Transalkylation
C9 + C6 ↔ C9
Transalkylator
Alkylator
TC
TC
LC
PC
LC
LC
PC
LC
LC
PC
TC
LC
PC
LC
TC
TC
FC
X
FC
X
TC
TC
FC
FC
X
X
CC
CC
TPM
FC
LC
TC

## Slide 8: Exercise: HDA Process
C7H8 + H2 → C6H6 + CH4
2C6H6 ↔ C12H10 + H2